This is the html version of the file http://www.pipavavrailway.com/docs/dscarticle.pdf.

Google automatically generates html versions of documents as we crawl the web.

Page 1

Date 29.05.2006

Introduction of Double Stack Container Train on IR- a Path Breaking

Achievement

By Naresh Kumar Vice- President (Technical), Indian Railway Service of

Mechanical Engineers (IRSME) , Pipavav Railway Corporation Limited

(PRCL)

WHEN OAKLAND global ocean carrier APL introduced technology to load rail cars

on top of each other in 1984, critics said it wouldn't work. To show the reliability of

its "stack train" technology, APL loaded a container with a dinner table, set it with

crystal, china and silverware, and railed it across the country. Everything arrived

intact. Still, not everyone was convinced.

Double-stack technology caught on as a cheaper way to move auto parts and

consumer goods across North America. The market has grown 100-fold since 1984.

As stack train celebrates its 20th anniversary, it remains an attractive alternative to

long-haul trucking, which has been hurt by rising fuel prices.

1. Indian Scenario

When Pipavav Railway Corporation Limited (PRCL) - a joint venture company of

Ministry of Railways (MOR) and a private port, Gujarat Pipavav Port Limited,

mooted the idea of running double stack with the existing flat wagons and existing

axle load of 20.32 tonnes in 2003, many people find it impossible thing and the

concept did not find favor in Rail Bhawan.

But with the change of guard in the Rail Bhawan in May 2004, the concept was again

given a try by PRCL. This time the everything was in favor of the concept and MOR

has taken keen interest in the implementation of this concept. Within a short time of

four months from the time of detailed study of the infringements, the first double

stack train has become the reality on Indian Railways on 23

rd

March 2006 between

Jaipur- Pipavav ( 950 Kms) .

Page 2

2. Why Double Stack?

The growth in containerized transport of trade volumes has shown a CAGR of 17.2%

against the overall growth of 8.6% at all Indian ports. In the post-liberalization era

(1991 onwards) container traffic has increased more than 7 fold. Container traffic,

besides registering the impressive growth, also covers a vast hinterland for each port

which calls for a transport infrastructure capable of providing sufficient capacity for

fast, cost effective service to Indian shippers and enable them to face the competitive

world markets.

•

The present rail share in container transport is around 27% and is not increasing

because of several reasons. Some of the reasons are the comparative benefits offered

by road transport: faster, door to door service, aggregation of smaller volumes, lesser

waiting time at ports and terminals, avoidance of additional handling of cargo at rail

terminals. All these help reduce costs in comparison to rail. Some of the problems

faced by railways in not matching these factors are related to existing constraints:

i.

IR has severe axle – load restrictions reducing the payload per unit of

transport. This affects throughput, cost of haulage and detention at

terminals

ii.

Lower speeds of goods trains’ increase transit time.

iii.

Freight rates for high rated cargo are consequently higher as compared to

roads as well in comparison to other countries.

•

Container traffic will increase to 14 million TEU’s per year in next ten years. The

number of trains required shall be 137 trains per day at the present level of 30% rail

share. If the rail share is to be increased to 50 %, the trains required shall increase to

225 a day. This magnitude can not be handled with current bottlenecks and line

capacity constraints.

•

Container traffic will increase to 14 million TEU’s per year in next ten years. The

number of trains required shall be 137 trains per day at the present level of 30% rail

share. If the rail share is to be increased to 50 %, the trains required shall increase to

225 a day. This magnitude can not be handled with current bottlenecks and line

capacity constraints.

•

In India, presently Mumbai is the epicenter of the Container traffic. Out of a total

4.5 million TEUs handled at all ports during 2004-05, 2.37 MTEUS (53%) were

handled at JNPT/NSICT ports alone. The rail share from JNPT/NSICT had been 26 %

of which 80 % was for Northern hinterland which translated into 8 trains per day each

way on Mumbai- Delhi route. At this growth rate, JNPT/NSICT are likely to handle

900000 TEUs for Northern Hinterland in 2006-07 requiring 15 trains to be run each

way to and from Delhi area. It may increase further with the operation of 3rd berth at

JNPT, which is likely in Sept 2006.

•

Such line capacity constraints can not be eased overnight. Delhi- Mumbai freight

corridor will take time. Therefore there is an urgent need to think of strategies to give

immediate relief. Running Double Stack Container trains on non electrified routes is

one such feasible strategy.

Page 3

•

The ports of Mundra, Pipavav and Kandla in Gujarat are connected to the entire

North hinterland of Rajasthan, Haryana, Delhi, Punjab and Himachal Pradesh by non

electrified rail routes. These ports are projected to handle around 7,00,000 TEU’s in

2009-10. This will further go up to 1.6 million TEU’s in 2014-15. A noteworthy

feature of these ports is a very high coefficient of rail share; against 26% from JNPT,

Pipavav and Mundra have a rail share of more than 93%.

•

Ports of Pipavav, Mundra and Kandla will generate 17 trains in 2009-10 and 43

trains by 2014-15. These numbers will find it hard to move.

AJMER

JODHPUR

RATLAM

NEW DELHI

BIKANER

AMBALA CANTT

MUMBAI

KOTA

MAHARASHTRA

MADHYA PRADESH

GUJARAT

RAJASTHAN

U

DELHI

HARYANA

UTTARANC

PUNJAB

LUNI

RINGAS

MATHURA

PHULERA

MARWAR

SAMDARI

BHILDI

PALANPUR

MEHSANA

VIRAMGAM

GODHRA

NAGDA

BOTAD

SAMAKHIALI

SURENDRANAGAR

LUDHIANA

DHURI

HISAR

GURGAON

AHMADABAD

PIPAVAV PORT

KANDLA PORT

MUNDRA PORT

MERTA ROAD

REWARI

JAIPUR

BATHINDA

GARHI - HARSARU

GANDHIDHAM

ADIPUR

TUGLAKABAD

SURAT

HAZIRA PORT

JNPT

VASAI

LEGEND:

POTENTIAL DOUBLE STACK ROUTE

ELECTRIFIED LINE

DHANDARI KALAN

ANAND

BARODA

PORTS

DIESEL - NON-DSC

PHASE 1

Page 4

3. Advantages

DSC train operation has been very advantageous in removing these constraints

and will reduce the unit cost of transportation. The main advantages of DSC

operation are as under;

a) Number of trains can be reduced by 48%, for the same throughput.

b) The payload capacity of the container train has been increased from 1500 MT

to 2500 MT to match the carrying capacity of the locomotives.

c) The terminal congestion can be minimized. Dwell time of containers at

terminals and ports shall reduce.

d) Matching of throughput for larger ships can be fulfilled in lesser time.

e) Cost of unit transportation will reduce. Indian Railways has already given

discount of 25 % on haulage cost for DSC movement.

f) Rolling stock requirement of locos and rail flats will reduce substantially.

g) Rail share will increase with the same rolling stock.

h) Will encourage direct service of bigger ships to Indian Ports.

i) Overall transit time of containers will reduce.

This justifies the need for carrying more containers per train by using the vertical

space by double stacking containers and optimizing the use of an alternative route to

highly congested JNPT- Delhi route.

A Macro level estimation of savings in various costs has been tabulated below based

on the total throughputs of Gujarat Ports.

2005-06

2007-08

2009-10 2014-15

Projected TEUs

200959

326671

483557 1239285

No of trains with SSC

6.5

10.5

15.6

39.9

No of Trains With DSC.

3.4

5.6

8.3

21.2

Saving in Rakes Ass. 17 % extra transit

time for DSC Trns

7.4

12.0

17.8

45.6

Saving in Cost of Rakes (Rs. Crs.)

88.7

144.1

213.3

546.7

Saving in Locos assu.17 % extra transit

time

2.5

4.0

5.9

15.1

Saving in Expenditure on

Loco account in Rs Crs.) / annually

1.20

1.95

2.88

7.39

Saving on Account of Maintenance of

Rakes in Rs Crs. / Annually

4.43

7.21

10.67

27.34

Saving in Fuel in Crs of Rs

9.1

14.8

22.0

56.3

Saving in Crew in Crs.of Rs.

2.4

3.8

5.7

14.6

Total Saving in revenue Expenditure

17.13

27.85

41.22 105.65

Total saving in USD (1USD=45 INR) in Million

3.80

6.18

9.15

23.4

Apart from above, savings on deferment of line capacity works, detention of boxes at

ports and ICDs, savings in the ICDs and manpower for running less

no of trains are to be accounted.

Page 5

This justifies the need for carrying more containers per trains i.e. using the vertical

space by double stacking containers and optimizing an alternative route to the existing

JNPT- Delhi route

4. How it has been done?

The Railways is considering the idea of running DSC trains from last 10 Years. The

first technical study on this concept was got done by PRCL through RITES in 2001,

for the diesel route connecting port of Pipavav , since DSC operation is not feasible

on electrified route because of restriction of vertical clearance. RITES has identified

three routes connecting Pipavav Port and indicated the numbers and location of the

fixed structure which shall infringe the DSC operation on these routes based on the

information colleted from Zonal Railways. The routes identified were as under;

i) Gurgaon- Rewari- Jaipur- Phulera- Mehasana- Surendranagar- Pipavav.

ii)

Gurgaon- Rewari- Jaipur- Phulera- Jodhpur- Luni- Samadari- Bhildi -

Mehasan- Surendranagar- Pipavav

iii) Gurgaon- Rewari- Ringas- Phulera- Mehasana- Surendranagar- Pipavav.

The comparative distance for Gujarat Ports is as under;

Distance in Kms

Route ( Port to Gurgaon)

Kandla

Mundra

Pipavav

Viramgam- Mehasan-Phulera- Jaipur

1144

1198

1233

Viramgam- Mehasan-Phulera- Ringas

1079

1134

1168

Bhildi- Palanpur – Ringas

1015

1070

-

Bhildi- Samadari – Jodhpur – Ringas

1094

1149

-

Viramgam- Mehasan-Marwar- Luni- Jodhpur-

Phulera- Ringas

1221

1276

1311

In the mean time Railway Board had engaged CANAC for the detailed examination

of this concept, using CIDA funds. They had given their inception report in Nov.

2004. They have suggested implementing the DSC operation in three phases. They

have recommended that new type of wagons should be designed and track should be

upgraded to higher axle loads for final phase implementation. They could not

conclude their study.

Since delay was taking place in implementation of this concept, PRCL has requested

MOR to give permission for carrying out the detailed physical survey on the Gujarat –

Pipavav existing BG route via Jaipur- Ajmer to identify the infringements and suggest

ways and means to modify the infringements obstructing the DSC operation.

Accordingly MOR has permitted to carry out the foot by foot survey for DSC

operation vide its letter dated 24.08.2005.

PRCL has conducted this survey from 25.09.2005 to 30.09.2005. PRCL has also find

out the possibility of running DSC trains on the existing wagons within the present

axle loads limitations.

Page 6

5. Physical Survey

The survey was done on the existing BG route from Gurgaon to Pipavav via Rewari-

Jaipur- Marwar- Palanpur- Mehasan- Viramgam- Surendranagar- Pipvav comprising

of Delhi, Jaipur, Ajmer, Ahmedabad, Rajkot and Bhavanagar divisions of Northern

Railway(NR) , North Western Railway(NWR) and Western Railway (WR)

respectively. The survey of routes connecting ports, of Mundra and Kandla beyond

Palanpur was not done since the alternative short route from Palanpur was under

gauge conversion. Other alternative route via Rewari- Ringas – Phulera is also

planned for Gauge Conversion.

6. Methodology of Survey

•

A box structure of more than double stack height having provision of varying the

height was fabricated in Loco Workshop, Ajmer, NWR. This box structure was

manufactured in two stages, one fixed portion and other movable portions from angle

irons. In order to reduce the weight of the movable structure only the thin plates were

welded at three places. The movement of the movable part is done with the help of

pulley and wire rope system. In order to reduce the cost of this box, the released

materials were utilized as far as possible.

PHOTO of BOX Structure

Page 7

•

This box structure was mounted in a BOXN wagon by welding the fixed part of

the box with bottom and sides of the wagon. The measuring device i.e. a calibrated

scale was mounted on one of the legs of the structure.

•

The train consisting of this test wagon, a locomotive and a brake van was run

throughout the route during day time under the escorts of concerned railway officials

and the team of experts from PRCL headed by Vice- President (Tech.), the Author.

•

The movable part of the box was raised manually at each structure and height of

the structure from the rail level was noted along with the span and width of the fixed

structures.

•

The locations of HT lines, LT lines, and telegraph lines crossing over the track

were recorded, during the run of this test train.

•

The survey was started from MADAR (AJMER), on 25.09.2005. The test train

reached Pipavav Port on 27.09.2005. Then the survey started from Ajmer on

29.09.2005 towards Gurgaon and reached Gurgaon on 30.09.2005. This survey was

completed in 6 days.

•

The team has taken the dimensions for 20 ROBs, 01 rail bridge, 31 FOBs , 01

water tank, and noted the location of 178 H.T. lines, 24 LT lines , 83 telegraph lines

and 66 telegraph posts.

The summary of the infringements is given below;

Particular

Gurgaon -

Jaipur ( KKU)

Jaipur- Pipavav

Total

As given

by RITES

ROB

10

10

20

9

Rail Bridge

1

0

1

0

FOB

11

20

31

22

HT Lines

3

19

22

51

LT lines

10

14

24

118

Telegraph lines

20

63

83

45

Signaling post

0

66

66

0

7. Oscillation Trails.

Research Design and Standard Organization (RDSO) has carried out the oscillation

trials with the existing BLC flat wagons. The trails have found successful upto the

maximum speed of 85 Kmph with 9-1/2’ high containers loaded upto the maximum

height with gross load of 30.5 MT each. These trials are conducted on the PRCL

section between DASA _ Savarkundla. They have tested 6 combination with various

CG heights . The brief for worst case parameters noted during the trails are as under;

A- Car

B- Car

No. Parameters

Max value

Speed

(KMPH)

Max value Speed

(KMPH)

1

Vertical Accl. (g)

0.299

85

0.547

85

2

Vertical RI

3.029

85

3.578

85

3

Lateral Accl. (g)

0.332

85

3.657

85

4

Lateral force Hy2m(t)

2.83

70

3.76

85

5

Derailment coefficient

0.60

85

0.49

60

Page 8

Based on the above results RDSO has drawn the following conclusion;

No adverse riding characteristics were noticed from the oscillation trail test data and

the pattern of oscillograms recorded for double stack container operation upto a

maximum speed of 85 kmph and the values of maximum RI, lateral force and

derailment coefficient were within the given limit. There was no resonance in the long

run.

8.0 Modification of Infringements

8.1 Infringements modified for Phase-1, (two 8-1/2’ high Cont.)

RDSO has developed an envelop for the straight track having height of 7300 mm and

width of 4360 mm for two 9-1/2’ containers without any restriction to the movement.

. For two 8-1/2 ‘ containers and A class ODC this envelop has been modified to 6500

mm height and 4360 mm width. Considering these dimensions the modifications have

been carried out.

For implementation of phase-1, part-1 DSC operation 6 no ROBs and 09 no. FOBs,

19 HT lines, 14 LT lines, 63 Telegraph lines and 66 signaling posts have been

modified. The details are as under;

ROB Modification

Location

Dimensions Tentative Cost

Suggested Method

1

BAR

(363.25Kms)

S=4.8m

B=6.75m

H=6035mm

82

The temporary LC has been built and the

existing ROB raised.

2

PNU

(652.25KMs)

S=23m

B=9.7m

H=5055mm

10

The traffic has been diverted on the adjacent

new ROB and the old has been broken.

3 MSH- Linch

(5/0Kms)

S=40.0m

B=21.0m

H=6160mm

05

On NH-8. The track has been lowered by 300

mm,

4

DASA

(22.7Kms)

S=4.8 m

B=7.5m

H=4995mm

200

Small ROB on State Highway. This ROB is

being raised although the traffic has been

diverted on the newly constructed LC. ROB

has been dismantled

5

SVKD(

64.93Kms)

S= 9.3m

B=7.5 m

H=5530mm

75

Small ROB on village road on cutting. This

ROB has is being raised and the traffic has

been diverted on the existing LC which is 0.5

kms away. ROB has been dismantled.

6

Rajula city

S=9.3

B=7.5

H= 6445

30

Small ROB connecting three- four houses of a

villages. Is being rebuilt.

Total cost in Lacs of Rs.

402 (0.89 Mn USD)

FOB Modification

Station

Ht in

mm

Tentative Cost

Suggested method

1

FL

5310

5.0

Has been raised

Page 9

2.

Kishangarh

6425

0.00

Track has been adjusted

3

Madar

6430

0.00

Track has been adjusted

4

RANI

6400

6.5

FOB has been raised.

5

Abu Rd.

5860

5.00

Fob has been dismantled and now being

raised.

6

PNU-1

6340

0.00

Track adjusted

7

PNU-2

6450

0.00

Track has been adjusted.

8

MSH

4995

1.0

FOB has been dismantled

9

Viramgam

6410

0.00

Track has been adjusted.

Total cost in Lacs Rs.

17.50 (0.03Mn USD)

Modification of other Infringements

Zone

NWR

WR

PRCL

Total Unit Cost

Rs Lacs

Tentative Cost

Rs Lacs

Sections

Jaipur-

Madar

Madar-

Palanpur

Palanpur-

SUNR

SUNR- PPSP

HT LINES

0

1

12

6

19

10

190

LT Lines

6

6

2

0

14

1.0

14.0

TEL. Lines

14

25

21

3

63

0.25

15.75

Sig. posts

24

0

42

0

66

0.00

0.00

Total Cost

219.75

(0(.48 mn USD)

Hence for commencement of DSC train from Jaipur to Pipavav and further connecting

to Mundra and Kandla, it has costed approximately, Rs 640 lacs, for implementation

of DSC with 8-1/2 ‘ containers.

After modification of the above infringements the first Double stack Train has been

inaugurated by Hon’ble Minister for Railways, Government of India.

Page 10

8.2 Infringements to be modified for Phase-1, (for two 9-1/2’ containers)

For implementation of part-2 of phase-1, 6 nos. ROBs, 16 nos. FOBs has been to be

modified, the details are as under;

ROBs

Location

Dim.

Cost in

Lacs

Method

1

Kishangarh

S=24.9 m

B=24.0m

H=6600 mm

15.0

Track is being lowered, by 700 mm

2

PNU

S=32m

B=11.7m

H=6635mm

15.0

Track is being lowered by 450 mm

3

MSH

S=40.0m

B=21.0m

H=6160mm

15.0

Track is being lowered 1200mm

4

Siddhpur

H=6900mm

15.0

Track is being lowered by 400mm

5

Limdi

S= 26m

B=34m

H=6510 mm

35.00

Track is being lowered by 600mm

Total Cost in Lacs of Rs.

95 ( 0.21mn USD)

FOBs

No.

Location

Vertical Ht.

Modification

Cost

1.

Kanakpura

6525

To be raised

2.5

2

Kishangarh

6425

To be raised

2.5

3

Madar

6430

To be raised

2.5

4

Marwar

6810

To be raised on goods

line

2.5

5

Falna

6520

to be raised

2.5

6

Sirohi Rd.

6510

to be raised

2.6

7

PNU-1

6340

0.00

8

PNU-2

6450

0.00

9

Palanpur

6450

raised on goods line

5.0

10

Siddhpur

7000

Train can be passed

11

Mehasana -1

6690

to be raised

2.5

12

Mehasana -2

6470

to be raised

2.5

13

Mehasan-3

6730

to be raised

2.5

14

Katosan Rd.

6440

to be raised

2.5

15

Viramgam

6410

Raised on line no.5 &6.

.2.5

16

Botad

6750

to be raised

2.5

17

Dhola

6860

to be raised

2.5

Total Cost in Lacs of Rs.

37.5(

0.08mn

USD)

Page 11

Hence the total additional cost for implementing phase-1, part-2 will be Rs.132.50.0

Lacs. The phase-1, part-2 can be implemented up to July 2006 at total cost of Rs 772

(1.71 Mn USD) Lakhs . While these costs were estimated by RITES as 10700 Lakhs

(23.7 mn USD) for less no. of infringements.

Indian Railway was even thinking of spending 200-300 Crores ( 45-65 Mn USD) of

Rupees on the Kandla- Delhi route for modifying the routes and increasing the axle

loads and thinking of designing of new wagons of well shape and tri- axle bogie.

8.3 Phase-2.

In the phase-2. Delhi area will be connected to all the Gujarat ports after the gauge

conversion of Rewari- Ringas- Phulera. The expenditure for modification of

infringements will be the part of this conversion cost.

For Phase-2, a mega ICD having facilities for handling DSC trains should also be

developed around Gurgaon / Rewari.

9. Comparison with USA

Double stack trains introduced on Indian Railways on flat has been a unique concept

This type of concept has been utilized for the first time in the world. The DSC train

movement on flat wagons is the most efficient way of double stacking as the payload

per meter length of the train is higher than US rail roads. I nave visited the US rail

roads and studied their double stack movement in detail. A brief comparison is done

in the table below;

Car Name

Pay Load Combination of

loading

Tare Wt Load per

axle

Ton

Wheel dia

in mm

No of

wgns 620

m. train

Teus per

train

3 Unit Draw bar

stack car

74

2X20’ /40’

Bottom, 40 top

25

25

838

36

144.

4 Unit Draw bar

stack car

75

Same

25

25

838

36

144.

Art. 5-unit -40’

Well Car

55

Same

17

36.

838- End

965- Art.

45

180

Flat Wagon of IR 61

Same

19.25

20.06

840

45

180

From the table above it is evident that the most efficient wagons i.e. Articulated 5-

unit 40’ well car can take the 180 TEUs equivalent to our flat wagons in the same

length as of our trains i.e. 620 meter, but the payload capacity is 55 tonnes and axle

load requirement is 36 tonnes. However, the train length on US rail roads is almost

three times to our train lengths.

Page 12

10. Recommendation for Indian Railways (IR)

• IR should plan our DSC operation on flat wagons, instead of well wagons.

• IR have got the wider gauge compared to North America. Hence our stability

criterion may be more liberal.

•

The increase in throughput is 100% as compared to 60 % in case of well

wagons. ( Without articulation)

•

The articulation concept may not be feasible due to the severe restrictions of

payload of the wagons. For our loading pattern we require at least 45-50 tons

of axle loads for articulated wagons.

• The new design has to be developed for well wagons.

• The cost of well wagons will be almost double that of flat wagons.

• The tare weight of the wagon will be 33% more compared to the flat car.

•

For our 100% DSC operation weight wise even 22.5 Tonne of axle load is

sufficient.

• IR should explore the possibility of enhancing the axle loads of present

wagons from 20.32 to 22.5 tons.

• Axle load beyond 25 Tonnes may prove counterproductive as for higher axle

loads the wheel diameter has to be increased

• The loop lengths for dedicated freight corridors should be as per present three

train lengths, so that hub- spoke system can be followed through railway

network. The switching stations fitted with modern technology should be

constructed near the major container ports and ICDS.

• Use of end of telemetry system should be encouraged in order to save time in

shunting operations.

11. Conclusion:

With the introduction of this concept on IR , the container transportation is going to be

cheaper substantially. The direction of transportation may also see a change in the near

future. It may not be surprising that JNPT which is the hub of container business may

loose its significance, particularly for the Northern India cargo which is more than 40

% of the total EXIM cargo in containers. The east coast ports may not be able to

attract the cargo meant for East Asian countries. The ports on Gujarat coast namely

Pipavav, Mundra and Kandla will become significant. This change will be in the larger

interest of nation.